## Slide 1: Lecture 7—Image Relaxation: Restoration and Feature Extraction ch. 6 of Machine Vision by Wesley E. Snyder & Hairong Qi
Notes: Note: To print these slides in grayscale (e.g., on a laser printer), first change the Theme Background to “Style 1” (i.e., dark text on white background), and then tell PowerPoint’s print dialog that the “Output” is “Grayscale.” Everything should be clearly legible then. This is how I also generate the .pdf handouts.

## Slide 2: All images are degraded
Remember, all measured images are degraded
  Noise (always)
  Distortion = Blur (usually)
False edges
  From noise
Unnoticed/Missed edges
  From noise + blur
original
image
plot
noisy
image
plot

## Slide 3: We need an “un-degrader”…
To extract “clean” features for segmentation, registration, etc.
Restoration
  A-posteriori image restoration
  Removes degradations from images
Feature extraction
  Iterative image feature extraction
  Extracts features from noisy images

## Slide 4: Image relaxation
The basic operation performed by:
  Restoration
  Feature extraction (of the type in ch. 6)
An image relaxation process is a multistep algorithm with the properties that:
  The output of a step is the same form as the input (e.g., 2562 image to 2562 image)
    Allows iteration
  It converges to a bounded result
  The operation on any pixel is dependent only on those pixels in some well defined, finite neighborhood of that pixel. (optional)

## Slide 5: Restoration: An inverse problem
Assume:
  An ideal image, f
  A measured image, g
  A distortion operation, D
  Random noise, n
Put it all together:
  g = D( f ) + n
This is
what we
want
This is
what we
get
How do we
extract f ?

## Slide 6: Restoration is ill-posed
Even without noise
Even if the distortion is linear blur
  Inverting linear blur = deconvolution
But we want restoration to be well-posed…

## Slide 7: A well-posed problem
g = D( f ) is well-posed if:
  For each f, a solution exists,
  The solution is unique, AND
  The solution g continuously depends on the data f
Otherwise, it is ill-posed
  Usually because it has a large condition number:
    K >> 1
Notes: ** Important for Registration **

## Slide 8: Condition number, K
K   output /  input
For the linear system b = Ax
  K = ||A|| ||A-1||
  K  [1,∞)

## Slide 9: K for convolved blur
Why is restoration ill-posed for simple blur?
Why not just linearize a blur kernel, and then take the inverse of that matrix?
  F = H-1G
Because H is probably singular
If not, H almost certainly has a large K
  So small amounts of noise in G will make the computed F almost meaningless
See the book for great examples

## Slide 10: Regularization theory to the rescue!
How to handle an ill-posed problem?
Find a related well-posed problem!
  One whose solution approximates that of our ill-posed problem
E.g., try minimizing:
  But unless we know something about the noise, this is the exact same problem!

## Slide 11: Digression: Statistics
Remember Bayes’ rule?
  p( f | g ) = p( g | f ) * p( f ) / p( g )
This is the
a priori pdf
This is the
conditional
pdf
This is the
a posteriori
conditional
pdf
Just a
normalization
constant
This is what we want!
It is our discrimination
function.

## Slide 12: Maximum a posteriori (MAP) image processing algorithms
To find the f underlying a given g:
  Use Bayes’ rule to “compute all” p( fq | g )
    fq  (the set of all possible f )
  Pick the fq with the maximum p( fq | g )
    p( g ) is “useless” here (it’s constant across all fq)
This is equivalent to:
  f = argmax( fq) p( g | fq ) * p( fq )
Noise term
Prior term

## Slide 13: Probabilities of images
Based on probabilities of pixels
For each pixel i:
  p( fi | gi )  p( gi | fi ) * p( fi )
Let’s simplify:
  Assume no blur (just noise)
    At this point, some people would say we are denoising the image.
  p( g | f ) = ∏ p( gi | fi )
  p( f ) = ∏ p( fi )

## Slide 14: Probabilities of pixel values
p( gi | fi )
  This could be the density of the noise…
  Such as a Gaussian noise model
  = constant * esomething
p( fi )
  This could be a Gibbs distribution…
    If you model your image as an ND Markov field
  = esomething
See the book for more details

## Slide 15: Put the math together
Remember, we want:
  f = argmax( fq) p( g | fq ) * p( fq )
  where fq  (the set of all possible f )
And remember:
  p( g | f ) = ∏ p( gi | fi ) = constant * ∏ esomething
  p( f ) = ∏ p( fi ) = ∏ esomething
  where i  (the set of all image pixels)
But we like ∑something better than ∏esomething, so take the log and solve for:
  f = argmin( fq) ( ∑ p’ ( gi | fi ) + ∑ p’( fi ) )

## Slide 16: Objective functions
We can re-write the previous slide’s final equation to use objective functions for our noise and prior terms:
  f = argmin(fq) ( ∑ p’( gi | fi ) + ∑ p’( fi ) )
    
  f = argmin(fq) ( Hn( f, g ) + Hp( f ) )
We can also combine these objective functions:
  H( f, g ) = Hn( f, g ) + Hp( f )

## Slide 17: Purpose of the objective functions
Noise term Hn( f, g ):
  If we assume independent, Gaussian noise for each pixel,
  We tell the minimization that f should resemble g.
Prior term (a.k.a. regularization term) Hp( f ):
  Tells the minimization what properties the image should have
  Often, this means brightness that is:
    Constant in local areas
    Discontinuous at boundaries

## Slide 18: Minimization is a beast!
Our objective function is not “nice”
  It has many local minima
  So gradient descent will not do well
We need a more powerful optimizer:
Mean field annealing (MFA)
  Approximates simulated annealing
  But it’s faster!
  It’s also based on the mean field approximation of statistical mechanics

## Slide 19: MFA
MFA is a continuation method
So it implements a homotopy
  A homotopy is a continuous deformation of one hyper-surface into another
MFA procedure:
  Distort our complex objective function into a convex hyper-surface (N-surface)
    The only minima is now the global minimum
  Gradually distort the convex N-surface back into our objective function

## Slide 20: MFA: Single-Pixel Visualization
0.3 |  |  |  |  |  |  |  |  |  |  | 
0.2 |  |  |  |  |  |  |  |  |  |  | 
0.1 |  |  |  |  |  |  |  |  |  |  | 
0 |  | 20 |  | 40 |  | 60 |  | 80 |  | 100 | 
Continuous deformation of a function which is initially convex to find the (near-) global minimum of a non-convex function.
possible values
for a single pixel
merit
of each
possible
pixel
value
initial
global
minimum
final
global
minimum
Notice that
we do not
end up here
or here

## Slide 21: Generalized objective functions for MFA
Noise term:
  (D( f ))i denotes some distortion (e.g., blur) of image f in the vicinity of pixel I
Prior term:
   represents a priori knowledge about the roughness of the image, which is altered in the course of MFA
  (R( f ))i denotes some function of image f at pixel i
  The prior will seek the f which causes R( f ) to be zero (or as close to zero as possible)

## Slide 22: R( f ): choices, choices
Piecewise-constant images
=0 if the image is constant
 0 if the image is piecewise-constant (why?)
  The noise term will force a piecewise-constant image
Notes: Derivative = 0 almost everywhere

## Slide 23: R( f ): Piecewise-planer images
=0 if the image is a plane
 0 if the image is piecewise-planar
  The noise term will force a piecewise-planar image
Notes: Clearly a better fit
(but not necessarily for, e.g., CT)

## Slide 24: Graduated nonconvexity (GNC)
Similar to MFA
  Uses a descent method
  Reduces a control parameter
  Can be derived using MFA as its basis
  “Weak membrane” GNC is analogous to piecewise-constant MFA
But different:
  Its objective function treats the presence of edges explicitly
    Pixels labeled as edges don’t count in our noise term
    So we must explicitly minimize the # of edge pixels

## Slide 25: Variable conductance diffusion (VCD)
Idea:
  Blur an image everywhere,
  except at features of interest
    such as edges

## Slide 26: VCD simulates the diffusion eq.
Where:
  t = time
  i f = spatial gradient of f at pixel i
  ci = conductivity (to blurring)
temporal
derivative
spatial
derivative

## Slide 27: Isotropic diffusion
If ci is constant across all pixels:
  Isotropic diffusion
    Not really VCD
  Isotropic diffusion is equivalent to convolution with a Gaussian
  The Gaussian’s variance is defined in terms of t and ci

## Slide 28: VCD
ci is a function of spatial coordinates, parameterized by i
  Typically a property of the local image intensities
  Can be thought of as a factor by which space is locally compressed
To smooth except at edges:
  Let ci be small if i is an edge pixel
    Little smoothing occurs because “space is stretched” or “little heat flows”
  Let ci be large at all other pixels
    More smoothing occurs in the vicinity of pixel i because “space is compressed” or “heat flows easily”

## Slide 29: VCD
A.K.A. Anisotropic diffusion
With repetition, produces a nearly piecewise uniform result
  Like MFA and GNC formulations
  Equivalent to MFA w/o a noise term
Edge-oriented VCD:
  VCD + diffuse tangential to edges when near edges
Biased Anisotropic diffusion (BAD)
  Equivalent to MAP image restoration
Notes: BUT, are the pieces separated where we want?

## Slide 30: VCD Sample Images
From the Scientific Applications and Visualization Group at NIST
http://math.nist.gov/mcsd/savg/software/filters/

## Slide 31: Various VCD Approaches: Tradeoffs and example images
Mirebeau J., Fehrenbach J., Risser L., Tobji S., “Anisotropic Diffusion in ITK”, the Insight Journal
Images copied per Creative Commons license
http://www.insight-journal.org/browse/publication/953
  Then click on the “Download Paper” link in the top-right

## Slide 32: Edge Preserving Smoothing
Other techniques constantly being developed (but none is perfect)
E.g., “A Brief Survey of Recent Edge-Preserving Smoothing Algorithms on Digital Images”
  https://arxiv.org/abs/1503.07297
SimpleITK filters:
  BilateralImageFilter
  Various types of AnisotropicDiffusionImageFilter
  Various types of CurvatureFlowImageFilter

## Slide 33: Congratulations!
You have made it through most of the “introductory” material.
Now we’re ready for the “fun stuff.”
“Fun stuff” (why we do image analysis):
  Segmentation
  Registration
  Shape Analysis
  Etc.